## Slide 1: Evaluation and improvement of a dual-channel method for the detection and quantification of high-temperature events on FireBIRD data
Penghua Li, October 04, 2017

## Slide 2: Contents
Introduction of MITIP, an atmospheric correction and image processing method
  Short description of MITIP
  Data preparation and pre-processing
  Outcomes of the MITIP
Validation and improvement of the MITIP
  Results comparison with MODIS SST and calibration
  Transferability test (SST)
  Results comparison with MODIS LST and calibration
  Transferability test (LST)
Analysis of high-temperature events
  High-temperature events
  Comparison with the results of Zhukov’s algorithm
Conclusion and outlook

## Slide 3: 1. Introduction of MITIP, an atmospheric correction and image processing method
The MITIP method is an atmospheric correction and image processing method developed by Dr.Rudolf at DLR, which is used for processing the thermal remote sensing imageries of the FireBIRD satellite.
MITIP firstly performs atmospheric corrections for the TET-1 imagery based on the water vapor column and elevation to get the ground surface radiance and temperature. Afterwards, a dual channel method is used to detect and characterize sub-pixel temperatures of hot pixels.

## Slide 4: 1. 2 Data preparation and pre-processing
Required input for MITIP:
  TET-1 scene with two bands: MIR as the first band, TIR as the second band;
  Water vapor file. Here we use MODIS water vapor products;
  Digital Elevation Models (DEM). ASTER Global Elevation map is used;
  Emissivity maps. Here we use the ASTER Global Emissivity Database;
All the above data is downloaded from the NASA’s websites. Most of them need to be converted to the GeoTIFF format firstly. According to the requirement of the MITIP, the input data should be 1) overlapped and 2) share the same numbers of rows and columns and 3) have same pixel size.
Here Python and GDAL are used to do the pre-processng.
  All input files and converted to the GeoTIFF format and reprojected into an appropriate UTM zone;
  All input files are resampling to pixel size 150 * 150;
  The TET-1 scene is used as mask to clip other imageries to ensure they are of same size.

## Slide 5: 1. 3 Outcomes of the MITIP
The outcomes of the MITIP can be divided into tow parts: one part is the result of atmospheric correction and another the high-temperature event monitoring products.
The results of atmospheric are:
  The “blackbody” surface radiance with ,
  The “graybody” surface radiance calculate from the input emissivity map and assuming ;
The result of high-temperature events monitoring is one GeoTIFF file which contains 6 bands:
  Band1: surface temperature in MIR band;
  Band2: surface temperature in TIR band;
  Band3: fire probability map;
  band4: effective target temperature in sub-pixel resolution;
  band5: effective target pixel fraction;
  band6: fire radiative power.

## Slide 6: 1. 3 Outcomes of the MITIP
Surface temperature map (MIR)
Surface temperature map (TIR)
Example: Bardarbunga 2014.09.14

## Slide 7: 1. 3 Outcomes of the MITIP

## Slide 8: 2. Validation and improvement of the MITIP
To see whether the temperature results derived from the MITIP is reliable or not, firstly we compare them with MODIS temperature products, namely MODIS Sea Surface Temperature (SST) and MODIS Land Surface Temperature (LST), to see its performance under normal temperature environments.
Here we select two test sites whose imageries mainly covered by sea (Etna) and homogeneous landscape (Libya) respectively.
Etna:
Libya-1:

## Slide 9: 2. Validation and improvement of the MITIP
The comparisons are done as follows (Etna as example):
The MODIS temperature products are reprojected into the same projection as TET-1 imagery, then resampled into same pixel size and clip into the same size as TET-1 imagery.
The differences of the temperature between the MITIP temperature results and MODIS temperature products are computed through the whole imagery.
Several (3 – 5) sub-areas which are cloud-free and homogeneous inside for all scenes of one test site are selected.
Outliers are filtered out and the mean of the temperature differences inside one sub-area are computed;
Finally, the mean values of all sub-areas’ are computed to denote the temperature difference between the MODIS SST and the results of MITIP of that scene.

## Slide 10: 2.1 Results comparison with MODIS SST and calibration
The emissivity map from ASTER Global Emissivity Database contains 5 bands. There are two bands, namely band 11 () and band 12 () fall in TET-1 imagery’s TIR band (). So there comes a problem which band of the emissivity map should be used. This problem would be considered under different circumstances.
Since the emissivities of water body in these two bands are very close, 0.984 and 0.985 respectively, the effects of different emissivities can be neglected when the results from MITIP is compared with MODIS SST. Here we use the emissivity map in band .

## Slide 11: 2.1 Results comparison with MODIS SST and calibration
Firstly, the temperature results from MITIP are compared with MODIS SST.
From the figure on the left we can see that the temperature derived by MITIP is a bit lower than the MODIS temperature products.
So the MITIP method add two input keywords and , which stand for scale factors for the MIR and TIR band respectively to calibrate the top of atmosphere (TOA) radiances of TET-1 imageries to adjust these differences.

## Slide 12: 2.1 Results comparison with MODIS SST and calibration
Since the temperature derived by MITIP is a bit lower than the MODIS temperature products, we need to increase the TOA radiances. Here we selected five scale factors, namely 1.00 (original TOA radiances), 1.05 (increase the TOA radiances by 5%), 1.10, 1.15, 1.20, for each band.
Scale factor 1.00
Scale factor 1.10
To see how the scale factor will affect the results of the MITIP, the histograms of the sub-areas in the surface teperature map of MIR band with different scale factors are investigated.
Firstly, we use the scene of 2014.06.22 and scale factor 1.00 and 1.10 as example.

## Slide 13: 2.1 Results comparison with MODIS SST and calibration
To make the shift more clearly, the histograms of sub-area 1 and sub-area 4 with all the five scale factor are shown on the right.
Sub-area 1
Sub-area 4
But we are not consider individual sub-area merely. Since the mean value over all sub-areas are used, the histogram of all pixels inside the 4 sub-areas are plotted and shown on the right.
Sub-area All

## Slide 14: 2.1 Results comparison with MODIS SST and calibration
From the histograms we can see that the mean temperature difference over all the sub-areas is a good characteristic to represent the the differences between the surface temperature maps from MITIP and MODIS temperature products and is suitable to use to do the comparison.
So in order to investigate a bunch of TET-1 scenes and do a time-series analysis, the method presented before, computing the mean of the temperature differences inside one sub-area and then the mean values of all sub-areas’ .

## Slide 15: 2.1 Results comparison with MODIS SST and calibration
The optimal scale factor for each band and its corresponding temperature difference is showed below.
According to the comparison results and analyses, the optimal scale factor for MIR band is chosen as 1.15 and for TIR band1.05.

## Slide 16: 2.2 Transferability test (SST)
The chosen scale factor should be tested with different TET-1 imageries. Here, it is tested using scenes of Etna, Demmin and Portugal as showed bellow.

## Slide 17: 2.3 Results comparison with MODIS LST and calibration
The similar comparison is done between the temperature results from MITIP and MODIS LST using scenes of Lybia-1.
However, emissivities of different land features vary a lot. So firstly we need to choose which emissvity map should be used.
With the experiences of the comparison with MODIS SST, here scale factors 1.15 for MIR band and 1.05 for TIR band are used as standard without affecting the results.

## Slide 18: 2.3 Results comparison with MODIS LST and calibration
Similarly, 5 sub-areas are chosen to do the comparison as showed in the picture on the right.
And different scale factors (1.00, 1.05, 1.10, 1.15, 1.20) are used to see the differences between the temperature results from MITIP is compared with MODIS LST. The results are showed on the right.

## Slide 19: 2.3 Results comparison with MODIS LST and calibration
We can see that this situation is very similar with the comparison with the MODIS SST. The optimal scale factor for each band and its corresponding temperature difference is showed below.
According to the comparison results and to keep consistence, the optimal scale factor for MIR band is chosen as 1.15 and for TIR band it is 1.05 as well.

## Slide 20: 2.4 Transferability test (LST)
The chosen scale factor would be tested with different TET-1 imageries. Here, it is tested using scenes of Libya-2.

## Slide 21: 3. Analysis of high-temperature events
After the analysis of performances of MITIP under the normal-temperature environments and the improvement of it, we get optimal scale factor for MIR band and TIR band respectively, namely 1.15 and 1.05.
Now, we are able to analyse the performances of MITIP on the monitoring of high-temperature events (HTE).
Firstly the results of the MITIP of the high-temperature monitoring is presented.

## Slide 22: 3.1 High-temperature events
Etna 2014.06.22

## Slide 23: 3.1 High-temperature events
Stromboli 2014.06.22

## Slide 24: 3.1 High-temperature events
Bardargunga 2014.09.14

## Slide 25: 3.1 High-temperature events
Portugal 2016.08.11

## Slide 26: 3.2 Comparison with the results of Zhukov’s algorithm
The Zhukov’s algorithm is the algorithm used to process the TET-1 imagery originally. It firstly filters clouds, water and other anomalies out and detects and quantifies the hot pixels later by means of per cluster instead of per pixel as the MITIP method does. After detection, Zhukov’s algorithm aggregates hot pixels which locates closed enough to form a hot cluster and calculate the characteristics such as temperature, cluster size of this cluster.
But the MITIP method performs a pixel-based analysis. Consequently, to do the comparison, a procedure is developed to shift the MITIP’s original pixel-based results to cluster-based results.

## Slide 27: 3.2 Comparison with the results of Zhukov’s algorithm
Etna 2014.07.21
Method | Temperature [K] |  |  | Cluster size
Zhukov | Min | Mean | Max | 127
 | 611 | 633.5 | 661.3 | 
MITIP | 644.3 |  |  | 123

## Slide 28: 3.2 Comparison with the results of Zhukov’s algorithm
Stromboli 2014.07.03
Method | Temperature [K] |  |  | Cluster size
Zhukov | Min | Mean | Max | 16
 | 504.6 | 529.9 | 564.9 | 
MITIP | 521.0 |  |  | 20

## Slide 29: 3.2 Comparison with the results of Zhukov’s algorithm
Etna 2014.06.22
method | Temperature [K] |  |  | Cluster size
Zhukov | Min | Mean | Max | 2461
 | 646 | 653.8 | 662 | 
MITIP | 661.3 |  |  | 2025

## Slide 30: 3.2 Comparison with the results of Zhukov’s algorithm
Etna 2014.06.22
loc | method | Temperature [K] |  |  |  |  |  |  |  | Cluster size
a | Zhukov | Min |  | Mean |  |  |  | max |  | 1804
 |  | 635.2 |  | 641.4 |  |  |  | 648.1 |  | 
 | MITIP | 656.7 |  |  |  |  |  |  |  | 2046
b | Zhukov | Min |  |  | Mean |  | Max |  |  | 3846
 |  | 617.6 |  |  | 626.9 |  | 637 |  |  | 
 | MITIP | 602.0 |  |  |  |  |  |  |  | 4500
c | Zhukov |  | Min |  |  | Mean |  |  | max | 3863
 |  | c1 | 612 |  |  | 615.2 |  |  | 618.5 | 
 |  |  |  |  |  |  |  |  |  | 3185
 |  | c2 | 612.9 |  |  | 619.9 |  |  | 627.5 | 
 | MITIP | 625.0 |  |  |  |  |  |  |  | 7829